## Slide 1: Quadruped Navigation using PPO and LiDAR in Unmapped Environments
4-Month Technical Progress Report
Presented by [Your Name], R&D Engineer
Date: [Insert Date]

## Slide 2: Agenda
1. Introduction & Motivation
2. Reinforcement Learning Basics
3. Why PPO for Quadruped Navigation?
4. PPO Math & Stability
5. Quadruped State, Action, Reward
6. LiDAR Preprocessing
7. PPO Network Design
8. Training & Results
9. Challenges
10. Future Work
11. Q&A

## Slide 3: Introduction & Motivation
Quadrupeds are suited for unstructured terrain.
Applications: search & rescue, logistics, military.
Challenge: Navigate dynamic unmapped environments.
Solution: Use RL with LiDAR (no pre-mapping).

## Slide 4: Reinforcement Learning Basics
Agent: Quadruped robot
Environment: Unknown terrain
State: LiDAR, velocity, orientation, goal vector
Action: Discrete velocity commands
Reward: Goal proximity, collision avoidance
Goal: Learn optimal navigation policy

## Slide 5: Why PPO for Quadruped Navigation?
Compared DQN, DDPG, TRPO, SAC
PPO: stable policy updates using clipped loss
Efficient training with good generalization
Less sensitive to hyperparameters than TRPO

## Slide 6: PPO Math & Stability
Policy Loss: L^CLIP(θ) = E[min(r_t*A_t, clip(r_t, 1-ε,1+ε)*A_t)]
Value Loss: L^V(θ) = 0.5 * (V(s_t) - R_t)^2
Clipping ensures stable policy updates
Advantage estimation improves learning

## Slide 7: Quadruped State & Action Design
s_t = {x_t, p_t, v_{t-1}, θ_t, α_t}
x_t: LiDAR scan, p_t: target vector
v_{t-1}: previous velocity, θ_t: yaw, α_t: angle to goal
Action: 7 discrete velocity/rotation choices

## Slide 8: LiDAR Preprocessing Methods
Method 1: 720 points → 120 sectors + one-hot orientation → 240D
Method 2: 30 points → min of 10 groups → 10D
Trade-off: Method 1 = high precision, Method 2 = faster

## Slide 9: PPO Network Design
Input: State vector (LiDAR + pose)
Hidden: Dense(1024 → 512 → 256)
Actor: 7 discrete velocity outputs
Critic: State value estimate V(s)
Both share initial feature layers

## Slide 10: Training Strategy
Randomized obstacles and goal placements
Curriculum learning: easy → complex
Use PPO loss + value loss + entropy
Metrics: reward, collisions, path efficiency

## Slide 11: Reward Function Design
R_total = α·R_goal + β·R_obstacle + γ·R_progress + δ·R_orientation
Negative distance to goal → approach reward
Penalty for obstacles → safer paths
Cosine orientation reward → alignment with goal

## Slide 12: Performance Metrics
Success Rate: 87.3%
Collision Rate: 2.1%
Path Efficiency: 1.34 (vs optimal)
Response Time: 23ms

## Slide 13: Challenges
Exploration vs Exploitation → entropy bonus
Sample Efficiency → domain randomization
Partial Observability → LSTM, state history
Dynamic Obstacles → adaptive policies

## Slide 14: Future Work
Real-world deployment trials
Add semantic input: cameras
Hierarchical planning layers
Transfer learning to new terrains
Multi-agent coordination

## Slide 15: Conclusion & Impact
Mapless PPO navigation successful
Streamlined method achieves 87% success
Real-time capable: 23ms decision latency
Applications: rescue, logistics, defense
Recommendation: Proceed to prototyping

## Slide 16: Q&A
Thank you!
Open for questions.